## Slide 1: Practical Parallel and Concurrent Programming
Course Overview
http://ppcp.codeplex.com/

## Slide 2: These Course Materials Brought to You By
Microsoft Research (MSR)
  Research in Software Engineering (RiSE)
University of Utah
  Computer Science
With support from
  MSR External Research (Judith Bishop)
  Microsoft Parallel Computing Platform (Stephen Toub, Sherif Mahmoud, Chris Dern)

## Slide 3: Courseware Authors
Thomas Ball, MSR Redmond
Sebastian Burckhardt, MSR Redmond
Ganesh Gopalakrishnan, Univ. Utah
Joseph Mayo, Univ. Utah
Madan Musuvathi, MSR Redmond
Shaz Qadeer, MSR Redmond
Caitlin Sadowski, Univ. California Santa Cruz

## Slide 4: Acknowledgments
This slide deck contains material courtesy of
  Tim Harris, MSR Cambridge
  Burton Smith, MSR Redmond
The headshot of the alpaca used throughout the lectures is licensed under
  the Creative Commons Attribution-Share Alike 2.0 Generic license
  http://en.wikipedia.org/wiki/File:Alpaca_headshot.jpg

## Slide 5: Overview
Context
  Trends
  Applications
  System and environment
Concepts
Units, Materials and Tools

## Slide 6: Technology Trends
Increasing parallelism in a “computer”
  multi-core CPU
  graphical processing unit (GPU)
  cloud computing
Increasing disk capacity
  we are awash in interesting data
  data-intensive problems require parallel processing

## Slide 7: Technology Trends (2)
Increasing networks and network bandwidth
  wireless, wimax, 3G, …
  collection/delivery of massive datasets, plus
  real-time responsiveness to asynchronous events
Increasing number and variety of computers
  smaller and smaller, and cheaper to build
  generating streams of asynchronous events

## Slide 8: Parallelism and Concurrrency: System and Environment
Parallelism: exploit system resources to speed up computation
Concurrency: respond quickly/properly to events
  from the environment
  from other parts of system
Environment
System
Events

## Slide 9: Application Areas
Entertainment/games
Finance
Science
Modeling of real-world
Health care
Telecommunication
Data processing
…

## Slide 10
Discuss application areas in context of
  Trends
  Parallelism/Concurrency
  System/Environment

## Slide 11: Practical Parallel and Concurrent Programming (PP&CP)
P&C | Parallelism | Concurrency
Performance | Speedup | Responsiveness
Correctness | Atomicity, Determinism, Deadlock, Livelock, Linearizability, Data races, … | 
P&C

## Slide 12: Overview
Context
Concepts
  Multi-core computer
  Speedup
  Responsiveness
  Correctness
Units, Materials and Tools

## Slide 13: Concept #1: System = Multi-core Hardware

## Slide 14: What is Today’s Multi-core?
What is the architecture?
What are its properties?
  Computation
  Communication
    Delivery guarantees
    Latency
    Throughput
  Consistency
  Caching

## Slide 15: A simple microprocessor model ~ 1985
Main memory
Processor core
ALU
1
2
3
4
5
...
Instruction stream
Clock: 0
Clock: 1
Clock: 2
Clock: 3
Clock: 4
Clock: 5
Clock: 6
Clock: 7
Clock: 8
Clock: 9
2
4
6
9
Completion time
Clock: 10
12
Clock: 11
Single h/w thread
Instructions execute one after the other
Memory access time ~ clock cycle time
Clock: 12
ALU: arithmetic logic unit

## Slide 16: FastFwd Two Decades (circa 2005): Power Hungry Superscalar with Caches
Main memory
Instruction stream
2
2
2
204 (main memory)
Completion time
226 (hit in L2)
Multiple levels of cache, 2 cycles for L1, 20 cycles for L2, 200 cycles for memory
ALU
ALU
ALU
1
2
3
4
5
...
L2 cache (4MB)
L1 cache (64KB)
Dynamic out-of-order
Pipelined memory accesses
Speculation

## Slide 18: Power wall + ILP wall + memory wall = BRICK WALL
Power wall
  we can’t clock processors faster
Memory wall
  many workload’s performance is dominated by memory access times
Instruction-level Parallelism (ILP) wall
  we can’t find extra work to keep functional units busy while waiting for memory accesses

## Slide 19: Multi-core h/w – common L2
Core
1
2
3
4
5
...
1
2
3
4
5
...
L2 cache
Core
Main memory
L1 cache
L1 cache
ALU
ALU
ALU
ALU

## Slide 20: Multi-core h/w – additional L3
1
2
3
4
5
...
1
2
3
4
5
...
Main memory
Single-threaded core
L1 cache
Single-threaded core
L1 cache
L2 cache
L2 cache
L3 cache

## Slide 21: SMP multiprocessor
Single-threaded core
1
2
3
4
5
...
1
2
3
4
5
...
L1 cache
Single-threaded core
L1 cache
L2 cache
L2 cache
Main memory

## Slide 22: NUMA multiprocessor
Interconnect
Single-threaded core
L1 cache
Single-threaded core
L1 cache
Memory & directory
L2 cache
L2 cache
Single-threaded core
L1 cache
Single-threaded core
L1 cache
Memory & directory
L2 cache
L2 cache
Single-threaded core
L1 cache
Single-threaded core
L1 cache
Memory & directory
L2 cache
L2 cache
Single-threaded core
L1 cache
Single-threaded core
L1 cache
Memory & directory
L2 cache
L2 cache
Notes: Tim Harris

## Slide 23: Three kinds of parallel hardware
Multi-threaded cores
  Increase utilization of a core or memory b/w
  Peak ops/cycle fixed
Multiple cores
  Increase ops/cycle
  Don’t necessarily scale caches and off-chip resources proportionately
Multi-processor machines
  Increase ops/cycle
  Often scale cache & memory capacities and b/w proportionately

## Slide 24: Concept #2: Speedup

## Slide 25: Speedup Concerns
Focus on the longest running parts of the program first
  be realistic about possible speedups
  different parts may need to be parallelised with different techniques
Understand the different resource requirements of a program
  computation, communication, and locality
Consider how data accesses interact with the memory system:
  will the computation done on additional cores pay for the data to be brought to them?
Notes: From Tim Harris:
The performance of one thread is highly dependent on what other threads are doing
It’s important to understand the h/w of the machine, and the techniques it uses
For modest numbers of cores, it may be possible to identify large granularity tasks, with good data locality
Understand the different resource requirements of a program; computation, communication, locality
Consider how data accesses will interact with the memory system; will the computation done on additional cores pay for the data to be brought to them?
Focus on the longest running parts of the program first; be realistic about possible speedups
Aim to tackle larger workloads in constant time (c.f. Gustafson’s law)
Exploit asymmetric designs; larger cores for sequential perf, smaller cores where high degrees of parallelism are available
Multiple parts of an algorithm may need to be parallelised with different techniques
With modest numbers of cores, beware of overheads that must be recovered via parallelism

## Slide 26: Abstractions for Speedup
Imperative parallelism
  Parallel.For/ForEach
  Lightweight tasks (not threads)
Functional parallelism
  Functional programming (F#)
  Parallel Language Integrated Queries (PLINQ)
  Array parallel algorithms (Accelerator)
Concurrent components
  for example, data structures that can efficiently accommodate many clients

## Slide 27: Concept #3: Responsiveness

## Slide 28: Responsiveness Concerns
Quick reaction to conditions over event streams
Handle multiple tasks at the same time
Don’t block essential tasks unnecessarily
Coordinate responses to requests

## Slide 29: Abstractions for Responsiveness
Asynchronous computation
  lightweight tasks (not threads)
  F#’s async
Application-specific scheduling
Complex event handling
  IObservable
  Reactive extensions (RX) to .NET
Actors/agents

## Slide 30: Concept #4: Correctness

## Slide 31: Correctness Concerns
All those we have for sequential code
  Assertions, invariants, contracts,
  buffer overflows, null reference,
  …
Plus those related to parallelism/concurrency
  Data races, deadlocks, livelocks, …
  Memory coherence/consistency

## Slide 32: Correctness Abstractions
Atomicity
Determinism
Linearizability
Serializibility
Temporal logic

## Slide 33: Outline
Context
Concepts
Units, Materials and Tools

## Slide 34: Units 1 – 4
Unit 1: Imperative Data Parallelism
  Data-intensive parallel programming (Parallel.For)
  Concurrent Programming with Tasks
Unit 2: Shared Memory
  Data Races and Locks
  Parallel Patterns
Unit 3: Concurrent Components
  Thread-Safety Concepts (Atomicity, Linearizability)
  Modularity (Specification vs. Implementation)
Unit 4: Functional Data Parallelism
  Parallel Queries with PLINQ
  Functional Parallel Programming with F#

## Slide 35: Units 5 – 8
Unit 5: Scheduling and Synchronization
  From {tasks, DAGs} to {threads, processors}
  Work-stealing
Unit 6: Interactive/Reactive Systems
  External vs. internal concurrency
  Event-based programming
Unit 7: Message Passing
  Conventional MPI-style programming
Unit 8: Advanced Topics
  Parallelization, Transactions, Revisions

## Slide 36: Unit Dependences

## Slide 37: IDE, Libraries, Tools, Samples, Book
Visual Studio 2010
  C# and F# languages
  .NET 4: Libraries for multi-core parallelism and concurrency
Other Libraries
  Accelerator
  Code Contracts
  Rx: Reactive Extensions for .NET
Alpaca
  A lovely parallelism and concurrency analyzer
  Source code
Code for all units, with Alpaca tests
Parallel Extensions Samples
Free book: Parallel Programming with Microsoft .NET

## Slide 38: Icon Guide
Aside
Performance
Concept
Run
Correctness
Concept
Code
Concept
Discuss
Alpaca
Project

## Slide 39: .NET 4 Libraries for Parallelism and Concurrency

## Slide 40: Alpaca: A lovely parallelism and concurrency analyzer
Atttribute-based testing, for performance and correctness concepts
[UnitTestMethod]
  simply run this method normally, and report failed assertions or uncaught exceptions.
[DataRaceTestMethod]
  Run a few schedules (using CHESS tool) and detect data races.
[ScheduleTestMethod]
  Run all possible schedules of this method (with at most two preemptions) using the CHESS tool.
[PerformanceTestMethod]
  Like UnitTestMethod, but collect & graphically display execution timeline (showing intervals of interest)
Alpaca
Project

## Slide 41: Why Alpaca?
Improve the learning experience for concurrent and parallel programming
Vehicle for including instantly runnable sample code (incl. bugs)
Unit tests: A quick way to validate / invalidate assumptions, about correctness or performance
Provide simple graphical front end for various tools

## Slide 42: PPCP – Unit X - *.sln
Each Unit has a VS2010 Solution
  supporting examples
  Alpaca Project

## Slide 43: Parallel Extensions Samples
http://code.msdn.microsoft.com/ParExtSamples
Over 15 Samples
  applications illustrating use of .NET 4
  some included in courseware
ParallelExtensionsExtras.csproj
  helper classes built on .NET 4
Run

## Slide 44: Sample: Ray Tracer
Animated, ray traced bouncing balls. Sequential and parallel implementations are provided, as is a special parallel implementation that colors the animated image based on which thread was used to calculate which regions.
Run

## Slide 45: Sample: Image Morphing
Implements a morphing algorithm between two images. Parallelization is done using the Parallel class.
Run
Notes: Not included in courseware, get as separate download

## Slide 46: Sample: N-Body Simulation
Implements a classic n-body simulation using C# and WPF for the UI and using F# for the core computation. Parallelism is achieved using the Parallel class.
Run

## Slide 47: Free book: Parallel Programming with Microsoft .NET
Design Patterns for Decomposition and Coordination on Multicore Architectures
Colin Campbell, Ralph Johnson, Ade Miller and Stephen Toub